## Slide 1: Cryogenic Classical Control Architectural Simulations
March 14, 2017

## Slide 2: Qubit Parameters

## Slide 3: Model Parameters
Thermal Zone Characteristics
Interconnect Hardware
Hardware | Power Dissipation | Latency
RF Coaxial Cable | P = λA(δT)/L | A: 10 ns (45K->4K) B: 1ns (4K->20mK)
HEMT Cryoamplifier | 4 mW – 12 mW | N/A
Electrical Attenutator | Passive | N/A
Zone | Capacity | Overhead
45K | 40 W | 10X
4K | 1.5 W | 200X
120 mK | 600 uW | 
100 mK | 400 uW | 
20 mK | 14 uW | 5 x 104 X
Control Interconnect Schematic
A
A
B
B

## Slide 4: CryoCMOS Model
Serial I/O
≥ 10ns Latency
Two Interconnects in/out of 20mK zone
MUX within 20mK – including DC bias

## Slide 5: CryoCMOS Controller Parameters
Serial I/O (JTAG + UART) 10ns latency/<bandwidth>
  Bandwidth: 1 bit | 1 byte
  1 bit: 640 ns/cycle: 1.5 MHz
  1 byte: 80 ns/cycle: 12.5 MHz
Operating Frequency
  700 MHz – MSFT
Power Dissipation
  10-15 J/operation
  100K logic elements
  Maximum: 70 mW
Operation
Charbon Control Schematic

## Slide 6: CryoCMOS Memory Parameters
I/O external memory latency
  10 ns / 1 byte
Cycle time
  1.42 ns = 1 / 700 MHz
Single instruction latency
  80 ns = 56 cycles
Cache line (single instruction) access time
  1 cycle
Cache miss penalty
  896 cycles = 16 lines x single instruction latency
Access Times
Power Dissipation
For a 64 KB cache size:
  12 mW per read
  21 mW per write
Rough estimates

## Slide 7: Normalization: Number of Required ECC Cycles
Each application – flattening configuration:
  Operational time steps (number of SIMD instructions)
  Cache behavior (hit rate, miss rate)
Number of ECC Cycles Required calculated by:
=

## Slide 8: Serial I/O Application Statistics Fully Flattened Applications
Chart: Application
| SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | Ising Model n100 | BWT | SHA-1 | Shors n4 | QFT n5 | Square Root
 | 40185 | 15811601 | 122934 | 2115940 | 2905 | 8543
 | 65 | 25299 | 197 | 3386 | 5 | 14
Serial I/O without internal memory requires many ECC cycles to execute applications with reasonable success probability (≥ 50 %)

## Slide 9: CryoCMOS Model with Memory
Serial I/O
≥ 10ns Latency
Internal memory with single instruction bandwidth, fast access time

## Slide 10: Internal Memory Application Statistics Unflattened Applications
Adding internal memory of 64KB shows a trade off: good caching requires low exposed parallelism
Chart: Application
| SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | Ising Model n100 | BWT | SHA-1 | Shors n4 | QFT n5 | Square Root
 | 2971767 | 19161401 | 2789256 | 7816993 | 4714 | 8619
 | 4265 | 177 | 214 | 40 | 3 | 1

## Slide 11: Internal Memory Application Statistics 100K Flattened Applications
Adding internal memory of 64KB shows a trade off: good caching requires low exposed parallelism

## Slide 12: Internal Memory Application Statistics 2M Flattened Applications
Only largely parallel applications benefit from flattening – smaller and more serial applications suffer drastically
Chart: Application
| SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | SIMD Instructions | ECC Cycles Required | Ising Model n100 | BWT | SHA-1 | Shors n4 | QFT n5 | Square Root
 | 41108 | 15811601 | 599636 | 2184041 | 2905 | 8543
 | 4761 | 46349 | 198 | 12499 | 8 | 30